## Project 1 documentation
Cryptography course at FIT BUT
Martin Krajňák, xkrajn02
### Introduction
The goal of this work is the explanation of the steps which lead to solution of the project. Initially, the work describe revelation of the first part of the encryption algorithm. The next part is dedicated to manual solution and total decryption of a secret used to encrypt files followed by the part explaining the solution achieved with SAT solver.
### Known plaintext attack
Since both plain-text (bis.txt) and cipher-test (bis.enc.txt) are available, then application of the XOR logical function reveal 512 B of keystream. Furthermore, by applying the keysteam to the encrypted sile super_cipher.py.enc, a step function used for encryption and SUB array are revealed. A function able to revert the step function needs to be implemented to decrypt files.
### Manual solution
Inspection of the revealed part of the super_cipher.py is showing two substeps. The first steps is adding 1 and performs bit operations which are shifting bits. The second step is again using bitwise shift operator to calculate an index to re-assign a new value from the revealed SUB array (substitution) for every bit in the . Therefore a reverse function must implement steps that are inverse to these steps in the reverse order. To reveal the original string used for keystream init we have to apply the reverse fuction 128 times.

A	B	C	S
0	0	0	0
0	0	1	1
0	1	0	1
0	1	1	0
1	0	0	1
1	0	1	0
1	1	0	1
1	1	1	0

Table 1: Truth table
The SUB array contains 7 items in total so we have 7 posibilities how to address the items in the array as described in the Table 1. The reverse process has to be done for every bit, so if we read the extracted secret from on of the encrypted files. After we read the first bit we are left with four possibilities as displayed in the table for both 0 and 1. At this state it is imposible to check which option will be the right one, therefore it’s necessary to track all four of them. Once the iteration is done for all bits on all four options, one of those four is the right reversation of the substituion. To find which one, the initila operation from the original step function has to be reversed – the add one and shift operation which is simply done by shifting the bits in the reverse order. After application of the reverse shift to the option, the step function can be called with the result and if it matches the original keystream from the input, the step reversal process was has been successful and the result is returned.
### SAT solution
This solution is implemented via satispy[1] library that is using a Minitsat[2] solver binary. The work with the library is for our use case is to create a Variable object for each bit of the keystream. The variable object contains two properties: name and reversed. Those variables are used to simulate boolean values.

Figure 1: Karnaugh Map
[1] https://github.com/netom/satispy
[2] http://minisat.se/
To get a solution, it is required to provide a formula for each bit of the keystream. Therefore a boolean expression in a DNF[3] need to be found for our problem. To achieve this, the Table 1 is converted to the Karnaugh Map displayed in Figure 1. From there there, the formula for True bits is (-a * -b * c) + (b * -c) + (a * -c) and for Flase bits (-a * -b * -c) + (b * c) + (a * c).
[3] https://en.wikipedia.org/wiki/Disjunctive_normal_form
 The library then converts the composed satispy object to Minisat solver binary which tries to provide a solution. If the solution was found, the result object is error and success boolean properies is received. If the solvet has successfully found the solution